## Slide 1: Burned Area Emergency Response Program BAER

## Slide 2: BAER PURPOSE
To identify imminent post-fire threats to life, safety, and property.
Critical natural and cultural resources resulting from the effects of a fire.
Take immediate actions to manage unacceptable risks.

## Slide 3: BAER
BAER is an emergency function and should be treated as such by the Incident Commander and Agency Administrator

## Slide 4: BAER and Wilderness Areas - permitted to prevent unnatural loss of wilderness resource or - to prevent protect life, property, and other resource values outside of wilderness

## Slide 5: BAER Policies
Forest Service Manual 2500, Chapter 2523, Forest Service Handbook, Chapter 2509
DOI, Department Manual, Part 620: Wildland Fire Management, Chapter 3
Interagency Burned Area Emergency Stabilization and Rehabilitation Handbook

## Slide 6: Rehabiliation Components
Suppression Rehabilitation
Emergency Stabilization
Rehabilitation
Restoration

## Slide 7: PROGRAM COMPONENTS
 | Suppression Rehabilitation | Emergency Stabilization | Rehabilitation | Restoration
Objective: | Repair suppression damages | Protect life and property | Repair damages | Long Term Ecosystem Restoration
Damage due to: | Suppression activities | Post-fire events | Fire | Fire
Urgency: | Before incident closeout | 1-12 months | 1-3 years | 3 + years
Responsibility | Incident commander | Agency Administrator | Agency Administrator | Agency Administrator
Funding type: | Suppression (fire) | Emergency Stabilization | Rehabilitation | Regular program
Notes: A final look at the reason, responsibility and funding for the different types of post-fire rehabilitation.

## Slide 8: Emergency Stabilization
Emergency stabilization treatments limited to 1 yr post fire from containment – recent policy change limits NNIS treatments to this
ES plans must be submitted within 7 days from containment, negotiable based on intent and complexity
Invasive species emergency stabilization must be addressed in a pre-existing management plan

## Slide 9: Rehabilitation
Rehabilitation treatments limited to 3 years post fire, must include monitoring
Rehab Plans should be completed within 7-10 days of containment, however could vary for each agency – contact BAER coordinator
Intended to repair or improve lands, natural, or cultural resources damaged directly by fire and unlikely to recover naturally

## Slide 10: Required Approvals

## Slide 11: FSM 2523.03
  Conduct assessments (FSM 2523.1) promptly on all burned areas following wildland fires to determine if emergency stabilization treatment is needed.
  An interdisciplinary process should be used when fires exceed 500 acres or when potential threats to life, property, natural resources, or cultural resources exist as a result of a smaller fire.

## Slide 12: FSH 2509.13 Responsibility of Team Leader
  Determine if a survey team is needed by conducting a reconnaissance survey
  If the reconnaissance survey shows that emergency rehabilitation is not needed or justified, document this conclusion on Form FS-2500-8 (Burned-Area Report), and recommend to the Forest Supervisor that the burned-area survey not be conducted and that emergency rehabilitation of burned-area survey is unnecessary.

## Slide 13: PHOTO

## Slide 14: PHOTO

## Slide 15: PHOTO

## Slide 16: PHOTO

## Slide 17: PHOTO

## Slide 18: FSH 2509.13 Responsibility of Team Leader
  If the reconnaissance survey shows that emergency rehabilitation is needed and justified, document this conclusion on Form FS-2500-8 (Burned-Area Report), and recommend to the Forest Supervisor that the burned-area survey team be formed .

## Slide 19: BAER ASSESSMENT TEAMS
Team Leader
Soil Scientist
Wildland Hydrologist
Plant Specialist
GIS specialist
Wildlife Biologist
Archeologist
Wilderness Resource Advisor
When formulating treatments and alternatives they provide invaluable input
Others depending on complexity
  NEPA, Forester, Operations,

## Slide 20: The Process
Complexity Analysis
  Size up Fire
  Burn Intensity Map
  Assess Effects
  Threats
Determine Team
Write Ops Plan
Write ESR Plan
Select Impl Ldr
Implement Specs
Monitor and Assess
Submit Reports

## Slide 21: Burn Complexity Analysis To determine the organization of the Planning Team
Preliminary Field Recon by Air or Ground
  Burn Intensity Map
  Acreage
  Vegetation Types and Resource Values
  Threats to Humans, Developments, Resources
  Land Owners and Jurisdictions

## Slide 22: Qualitative Indicators
Fire residence time can be judged by completeness of fuel consumption:
Low = black ashes
Moderate = grey or mixed ashes
High = white or red ashes

## Slide 23: Soil Hydrophobicity
Less than 1 minute = none
1-3 minutes = low
3-10 minutes = moderate
More than 10 minutes = high

## Slide 24: FIRE INTENSITY MAP AND THREATS

## Slide 25: POTENTIAL FLOODING & HIGH EROSION

## Slide 26: WATERSHED TREATMENTS

## Slide 27: Rodeo-Chediski Fire

## Slide 28: BAER TREATMENTS

## Slide 29: Wilderness BAER Treatments
Minimum necessary to address protection needs
Minimize intrusion of motorized equipment
Minimize introduction of NNIS
Leave area natural
Utilize native materials
Utilize materials or structures that area
temporary and plan for removal

## Slide 30: Slope Treatments
Notes: Log erosion barriers are also very labor intensive and are rarely prescribed on large areas.

## Slide 31: Channel structures
Notes: Structures may be installed in the top of the watershed to capture sediment.

## Slide 32: AERIAL SEEDING

## Slide 33: Straw Mulching

## Slide 34: RCW Cavity Inserts

## Slide 35: Invasive species treatments, Rehab Plan Loxahatchee National Wildlife Refuge
Section 3 Fire
June 25-27, 2001
9,000 acres

## Slide 36: IMPLEMENTATION LEADER
It is critically important that a project implementation leader be assigned to coordinate rehabilitation activities.
The first six months will be particularly complex and time consuming and should not be a collateral duty assignment.
Experience has indicated that the ability of the agency to quickly hire a project implementation leader will effect the overall success of the project.

## Slide 37: SUMMARY
BAER Mission:
The BAER program addresses short-term post-fire emergency situations with the goal of protecting life, property, natural, and cultural resources.
Why do we do BAER?
Post-fire hazards can KILL people and DAMAGE property and resource values.
Program Limitations:
BAER is not an opportunity to fix historic problems, expand programs or personnel, or conduct new surveys or long-term restoration.
BAER Program
Notes: Key notes:

## Slide 38: PRE-SEASON PREPAREDNESS
Select and maintain BAER team roster - team leaders, members, support personnel and trainees
Establish pre-planned treatment strategies
Keep current management direction accessible (LMP, Department Manuals, IA BAER Handbook, etc.)
Insure team readiness - safety, personal gear, availability status for on-forest and off-forest assignments, logistics, etc.,

## Slide 39: WHERE TO GET MORE INFORMATION
Regional Coordinators
Sue Wilder – USFWS
Emanuel Hudson – USFS
Caroline Noble – NPS

## Slide 40: WHERE TO GET MORE INFORMATION
Interagency Burned Area Emergency Stabilization and Rehabilitation Handbook
National Interagency Training Sessions
Field Operations Guide
NIFC Websites
BAER Briefcase CD

## Slide 41: DOI Web Site
http://fire.r9.fws.gov/ifcc/Esr/home.htm
USFS Web Site
http://www.fs.fed.us/biology/watershed/burnareas/